## Slide 1: Version 1.0 Design - Proteomics
Protein
Metadata
Peptide
PSM
Proteomics Quant
Protein
Metadata
PSM
Proteomics Ident
Complete vs Summary
Minor diffs at Meta Data level; Complete enforces assays and ms_run meta-data
Quant reported at assay and SV level in Complete; Summary allows quant at SV level only; only other difference is protein_coverage attribute enforced in Complete
Quant is optional at assay level in Summary files; so is search engine scores for every ms_run
No difference between Summary and Complete
Complete vs Summary
Only diff - Software optional in S;
Optional in S: protein_coverage; counts of PSMs, peptides; search engine scores per run
Peptide section should not be used (presume no support for peptide-level stats)
No difference between Summary and Complete
Quant vs ID diffs: No use of peptide section; Protein section leaves out Abundance columns;

## Slide 2: Proposed design change for proteomics in 1.1
Summary vs Complete distinction at present is rather pointless – seems fairly rare that studies will report quant only at SV-level but not at assay level
  What would be the use of this data? Cannot be used for statistics?
Distinction between ID and Quant file is mostly just the use of the quant columns – why not just make them null?
If distinction between Complete and Summary is desirable, why not split into Protein table vs all three tables are per proposed design in metabolomics 1.1 (following slides)
Downsides of this approach:
  Phospho-proteomics Summary file would not really work; but want to encourage most exporters to go for Complete files anyway, so long as reporting is not so onerous

## Slide 3: Metabolomics v1.1 Design
SML
Metadata
SMF
SME
Metabolomics Complete
“Final” quantified small molecules of interest e.g. including aggregation across adduct forms or different charge states etc
Features quantified in MS e.g. individual adduct form
Evidence stream for identification of molecule
SML
Metadata
Metabolomics Summary

## Slide 4: Proteomics v1.1 design-proposed
Protein
Metadata
Peptide
PSM
Proteomics Complete
“Final” quantified small molecules of interest e.g. including aggregation across adduct forms or different charge states etc
In case of ID only files, abundance columns are nulled; force exporters to add layer aggregating PSMs into peptides (e.g. mzIdentML already has a peptide section anyway, so this is really the same work)
1.0 specs imply that PSMs are mandatory for quant, which will be a big pain for some quant software; I would vote to make PSM table optional, say with a Boolean flag in the metadata for PSM_reported = “true|false” (MORE DISCUSSION NEEDED)
Protein
Metadata
Proteomics Summary

## Slide 5: Experimental design modelling replicates
Assay is in effect measurements made from a sample of interest, using MS
Different (bio or tech) replicates are modelled as different assays
Technical replicates usually multiple ms_runs
Assay 1
ms_run 1
Assay 2
ms_run 2
Assay 3
ms_run 3
Sample 1
Sample 1
Sample 1
mzTab 1.0 specs:
Clear definitions of biological and technical replicates are difficult to provide as these are somewhat dependent upon the biological domain. However, we use the following general definitions in mzTab.
Biological replicates are where different samples have been analyzed by MS.
Technical replicates are where same samples are analyzed multiple times by (LC)-MS.

## Slide 6: Experimental design label-free with no pre-fractionation (proteomics or metabolomics) – 3 tech reps
Study Variable 1
Assay 1
ms_run 1
Assay 2
ms_run 2
Assay 3
ms_run 3
Study Variable 2
Assay 4
ms_run 4
Assay 5
ms_run 5
Assay 6
ms_run 6
Sample 1
Sample 1
Sample 1
Sample 2
Sample 2
Sample 2
Samples are always optional and can have additional attributes

## Slide 7: Experimental design label-free with no pre-fractionation (proteomics or metabolomics) – 3 bio reps, no tech reps
Study Variable 1
Assay 1
ms_run 1
Assay 2
ms_run 2
Assay 3
ms_run 3
Study Variable 2
Assay 4
ms_run 4
Assay 5
ms_run 5
Assay 6
ms_run 6
Sample 1
Sample 2
Sample 3
Sample 4
Sample 5
Sample 6

## Slide 8
Study Variable 1
Assay 1
ms_run 1
Assay 2
Assay 3
Sample 1
Sample 2
Assay 4
Experimental design Duplex SILAC 2 tech reps
ms_run 2
Study Variable 2
mzTab 1.0 is unclear on what SV quants should include in this case
Assay quants are supposed to encode ratios as “raw quant values”. At protein-level, this would imply ratio could/should be encoded as follows, but it is unclear:
A1 A2 A3 A4 SV1 SV2
Protein 1 1 2.7 1 2.8 1 2.75
Protein 2 1 3.1 1 3.4 1 3.25
SILAC and iTRAQ mzTab 1.0 files show actual abundance quant values for all assays, but this is not the true data from most software approaches (SILAC at least), often uses median peptide ratio, so it is not meaningful to put raw quants in via this mechanism

## Slide 9: Question – encoding bio versus technical replicates?
Issue #30 on GitHub
Seems hard to encode at SV, assay or ms_run level
  Assay and ms_run can be re-used within file for different designs
  SV could say whether it contains bio and/or tech reps, but seems hard to flag which is which
Given this is complex – seems that enforcing if exporters wish to communicate a distinction between bio and tech reps, can be done via the multiplicity of connections to samples as on previous slides

## Slide 10: Problems with supporting pre-fractionation
Problem
A row in the Peptide table has “retention_time” and then assay (and SV) quants.
Assay can only be linked to 1 ms_run
ms_run is supposed to be designed to allow for multiple fractions inside it
  But – this looks like it was never implemented, since it can only have 1 location
Also, then impossible to say which fraction (or MS file) the Peptide came from
Same problem at PSM level
Same problem in SMF table
Same problem in SME table
Possible solutions
Peptide, PSM and SME currently have a spectra_ref column intended for referencing MS2 spectra (for MS2 peptide quants in that case)
  Could overload the use of this to capture fraction ID as well
  ms_run[1]-[1] where second field is fraction ID
  ms_run[1]-[1]-location
  ms_run[1]-[2]-location etc
Could add a column to each table for fraction ID, then come up with some way of encoding raw file locations etc in metadata?

## Slide 11: In case of pre-fractionation, what is ms_run?
mzTab 1.0 specs: “MS run – An MS run is effectively one run (or set of runs on pre-fractionated samples) on an MS instrument, and is referenced from assay in different contexts.”
Given we have concept of assay to capture complete set of measurements to be grouped together, do we need the concept of ms_run as a grouped set of MS instances?
Protein table has “num_psms_ms_run[1-n]” – unclear why this is not per assay, and just treat it like a label-free?
ms_run could thus default to being file location and other attributes?
However, even under this design, would still need to talk about fractions in the Peptide and SMF table… especially if fractionated samples have then been aligned -> can’t give a single ms_run value per row
MORE WORK NEEDED